Synchronizing PC and 01v96 both ways Studio Manager.

1. Open SM>File>Setup>Modify Workspace tab, you should see in the Device Editor window pane 01v96 and on the left Workspace window pane, 01v96. If you don't click on 01v96 on the left and Add to Workspace pane on the right.

2. Under MIDI Ports tab>Enable YAMAHA USB IN 0-1 [01v96]>Output Ports>Enable YAMAHA USB OUT 0-1. Under Preferences>Enable Automatically synchronize on file load>click Apply+OK.

3. SM again, File>Re-map midi ports, inputs and output ports should now show YAMAHA USB IN 0-1 [01v96] under Input ports workspace and system and YAMAHA USB OUT 0-1 under Output Ports workspace and system. If not add them from the drop down menu in each window. Close.

4. Double click the 01v96 icon in SM>you should see 01v96 Editor open>File>System Setup>Input port>change Not Assigned to YAMAHA USB IN 0-1>Ouput port>change Not Assigned to YAMAHA USB OUT 0-1. Channels Select>check both boxes PC->Console and Console->PC.  Layer Select>check both boxes and Window Control from console if you want to use the UD keys for assigning windows in SM opening and closing on the UD's. Store, Recall and Patch Confirmations are a preference, but I leave them unchecked as it makes saves a one button push.

If you don't see ONLINE in green at the top of your master channel strip, Rename from Untitled and Save SM as a YSM file to your desktop>reboot the computer, you should see, the green ONLINE now when you reopen your newly saved YSM file and can synchronize console to PC or PC to console. Most PC's need to be rebooted after assigning the Yamaha USB ports, don't forget thisthe reboot if you aren't getting syncrho by this time.

If you still don't get a USB connection and it says OFFLINE in yellow at the top of the master strip, close SM and go to Settings>Control Panel>MIDI Driver, you may have more than one of these, open the one that has the current Yamaha USB driver, mine says 2.1.4>Make sure that you have Thru ON/OFF "disabled". It should look like this:

Reboot the computer again. You should have sync both ways now.

Keep On Trackin'

------Ronny Morris - Digitak Mastering------
--------- www.digitakmastering.com ---------
-----------Powered By Experience-------------
-------------Driven To Perfection---------------

------Wink's Spam Free Audio Forum-----
---- http://63.231.68.228/smf/index.php ---
----------------------------------------------------------