Speaker Array Time Aligning With X-Over Information

Hi

Of course the ms is 1000th of a second .If you take the average speed

of sound 1130 feet per second > Divide 1000 by 1130 and you will

get .8849... ms per foot . My dsp crossover averages to .89ms when

one foot is entered .

My current midrange on one system need .72 ms to align at the

crossover point .

On my horn loaded mid system I need to delay the horn to the Midrange as it is farther back . Then sub to mid as well .

Also speaker rise time and crossover group delay add delay to the

equation as well .

A heavey 15 or 18 is slow in responing to the first impluse compared

to a lower mass mid or high . I have measured subs woofers that were

the same forward to back as the mids and yet were a full 5.5 ms back

in time from the midrange !

If you have hornloaded subs they could have a horn lenth of 6 feet or

more . I am sure you can see how far they may be out if this system

has front loaded mids .

Of course .72 ms might seem small but if you look at the wave lenth

at the crossover point it is a large amount . Wave lenths are I

believe the speed of sound divided by freq in question . If to make

it easy your crossover point is 1130 hz for the horn . The wave lenth

is 1 inch . It is very easy to get 100% cancelation if you alignment

is only 1/2 inch off . Of course the wavelenths around the crossover

point are still being reproduced by both drivers . Depending on wave

lenths there could be 1/2 cancelations. Some combining . Basic comb

filering around the crossover point . Ever hear that swish sound when

waking around a speaker ? Or two speakers close together with horns

overlapping in coverage not aligned correctly ?

Here is what I do .

With smaart I do a impluse time with each pandpass .

I find the pandpass that is farest back in time and add delay to the

other bandpasses to have their impluse times reach the measurement

mike together . Then I plot their phase angle at the crossover point

and fine tune the out of time bandpasses till their phase angle is

the same at the crossover point as the "reference" bandpass .

Then I delay the backline to the stacks .

I take the loudest source on stage . Say the snare in the current

band . I delay the mains so the sound of the snare reaches the

interset line of the mains at the same time as the sound goes out

them.

If you were to tie a string from one stack to the other this would be

the Zero point . To make it easy . Lets say it is 10 feet from the

snare straight out to the string . We know that sound takes 8.9 ms to

travel 10 feet . ( .89 times 10 equals 8.9 ms ) If I add 8.9 ms to

the dsp now the front stack is delayed to the loudest point from

stage . Also It is important to remember to subtract the latency of

the mixer and the dsp crossover . Say 1.2ms for the board and 1.8 for

the digital crossover so you would subtract 3 ms because the delay is

already in the signal path . Or 5.9 ms total now on the mains delay .

Now when the sound of the snare reaches the string it just starts

coming out the speakers . This tightens the sound . Giving better

focus to your mix .

Doesn't the V have delay on each channel ? I guess I could now delay

each channel to the string regards of volume ....?

Of course I use smaart to get right on the money . But averaging with

a tape and .89ms per foot gets you close . I will add a link or two

to give you a better explantion as I am strugling with the

conversion .

http://support.siasoft.com/Downloads/binary/TechNotes/CaseStudy6/case6

.pdf

http://www.siasoft.com/

The second is the home page .

You could look at the case studies and tech notes .

You may achive better sound by aligning your channels to the

Zero "string" point . Just remember to account for the channel or

main out delay if you are recording . ;-)

Doug