FX ROUTING - PHONES WET - RECORD DRY

I have resolved one of my outstanding, "How the heck do I route this 
like this", questions. That would be "How the heck do I route a wet 
signal to the phones but record dry?"

I uploaded my config file to the Files section. I did a simplified 
implementation so you would not be misled by a bunch of settings 
that had nothing to do with achieving the result.

A little background might be helpful for those interested. For this 
configuration I had a mike plugged into AD1. My headphone amp is 
connected to the Stereo Outs. The Monitors are connected to the 
Monitor Outs, and I record/playback via the ADAT i/o's.

You can control how much of an effect is sent to the Stereo/Monitor 
outs by adjusting the Send level for each analog input. These 
effects are not routed to the ADAT i/o's so the recorded signal
is dry as is the monitoring of any recorded tracks. For this example 
I exaggerated the effects.

Here are some brief steps I took to create the config file:
1.) Start in Fader Mode Home, Layer 1-16
2.) Ch1 On - Gain = 0db
3.) ST IN 1 & 2 On - Gain = 0db
4.) Press Fader Mode>Aux1 until "View1-16"
5.) Raise Ch1 Fader to 0db (Aux1 effect send level)
6.) Press Fader Mode>Aux2
7.) Raise Ch1 Fader to -15db (Aux2 effect send level)

The reason this did not work for me before was mostly because of 
step 3. I was raising the ST In levels while in the Aux mode. This 
has to be done when in the Home View. Off the top of my head the 
only other thing I did prior to the above was I went into 
Patch>Effect and assigned Reverb Stage to Aux1 and Delay LCR to 
Aux2. You can use also use Aux3&4 and apply the above steps to all 
AD channels.

If anyone has questions, please let me know. The next step would be 
to change this same config so that the wet signal gets recorded 
also. If you figure that out before me, please let me know. Chances 
are if I want to record effects from the v96 I'll assign them 
individually to an input but I'd still like to know how to do it 
across all inputs via the AUX bus.

I hope this is of value to someone.

Hi Miguel,

No doubt it will be. I'm going to start a FAQ's for the Files section and yours will be the first entry. They can download the Lib file that pertains to the FAQ article.

I loaded your session file in with no problems and can hear the verb and LCR. I swapped the fx with the LCR changed to mono delay and changed the stage verb to a hall, re-tweaked the param val's. Saved them on both fx. Than recalled them opposite, so that the delay is on FX-1 processor and first in the chain and the hall is on FX-2. I than added some pre eq comp and eq'd for my Audix stage mic. Saved the channel scene for next band practice to see how it sounds.

This is actually working out pretty cool, once we all get a little more familiar with the Yam 96k consoles, anyone having a routing problem won't have to be instructed step by step, we can just send them the I/O patch. Session and Lib files so far have been under 1KB in size and peeps with slo-mo's will get the files instantly. Of course, it's not going to help a newbie to learn the routing on his own, but it will be easier to show someone how to do it, if they can see the final result. I hope it doesn't make some of them lazy and just rely on the more experienced to set their patches. :O)

Glad that you got your wet monitor, dry record config. going. :O)

Keep On Trackin'

Ronny