Volume Squelch Pot Replacement Instructions For The Pro-97

Tools needed

small flat blade screwdriver

phillips screwdriver

soldering iron

solder

remove the four screws from the back of the scanner

Disconnect the speaker

Seperate the two boards(receiver and keypad/display

remove the top panel lock ring on the pot with a small flat blade screwdriver (jewlers),

then gently pull on the panel to remove it

desolder the antenna connection (both outer and inner),underneath the metal plate that the antenna connector sits on is a small phillips head screw.remove that

loosen the screw from the board that you desolder the antenna connector from,the metal plate will come off.

Desolder the 8 pins on the defective pot,make sure your joints for the new pot are not coated in solder,that will bend the pins.

Mount the new pot,solder them in and it will be good as new