I promised to document the HD24 diagnostics mode I fell into so ---
I didn't get to my document that I promised but (at least with version
1.18)......

Hold down track arm buttons 1 and 7 while powering up the HD24. Wait until
diagnostics come up. (Right after the Alesis HD24 announcement)

Scroll through the tests using FF and RW. PLAY to run the tests. Stop to
stop it.
Up Down arrows do some adjusting. I have played a lot and had intended to
write a more full featured version of this document.
The most useful test for me so far.....
Now you have a lot of tests including 1 kHz and 440 kHz tones on 24 channels
or single channels. 0 dBfs (use up down to adjust down then up -15 dBfs is 0
dBm? on an analog meter. (+4)

I take no responsibility for anything you may do with this information. I
learned it by "pushing buttons" based on old ADAT tape diags, etc. for a
long time.

I still anticipate writing a printable full featured version.

Peace and Music,

Francis



----- Original Message -----
From: "Jim Gilliland" <gilliland@...>
To: <hd24@yahoogroups.com>
Sent: Monday, April 11, 2005 5:41 PM
Subject: Re: [hd24] Re: Need Help with dd in Linux to recover audio SUCCESS!